## Slide 1: Attacking Smart Irrigation Systems IoT Village @ DefCon 26 11/08/2018
Fujitsu System Integration Laboratories

## Slide 2: Who Are We?
Ben Nassi is a Ph.D. student in the Department of Software and Information Systems Engineering at Ben-Gurion University of the Negev and a former Google employee. His Ph.D. topic is titled, "Cyber security in the IoT era."
Prof. Yuval Elovici is the director of the Telekom Innovation Laboratories at Ben-Gurion University of the Negev, head of BGU’s Cyber Security Research Center, and a professor in the Department of Software and Information Systems Engineering at BGU.
Dr. Asaf Shabtai is an assistant professor in the Department of Software and Information Systems Engineering at Ben-Gurion University of the Negev (BGU).
Moshe Sror is a security researcher at BGU’s Cyber Security Research Center. He holds a B.Sc. in software and information systems engineering from Ben-Gurion University of the Negev.
Fujitsu System Integration Laboratories

## Slide 3: Agenda
Smart Irrigation Systems
Reverse Engineering
Spoofing Attacks
Replay Attacks
Discussion

## Slide 4: Irrigation Systems – History & Evolution
2013
Smart irrigation systems appear
2016
First smart city adopts smart irrigation systems
Up to 2012
Traditional
irrigation systems
Today
Many vendors
Many connected sensors
GSM editions

## Slide 5: Smart Irrigation Systems
Smart irrigation systems are advanced irrigation systems that incorporate various sensors and network components for increased efficiency in order to save water and money.
Connected to the Internet.
Provide remote command & control service.
Allow automatic adaptation of watering plan based on the weather forecast.
Monitor watering plans and water consumption.

## Slide 6: Motivation for Buying Smart Irrigation Systems
Low price
Green technology
Very convenient UI
Remote control capability from smartphones, PCs, etc.
Enable sensor connectivity
Wireless connectivity (Wi-Fi and GSM)

## Slide 7: Ecosystem
Cloud Server
C&C Devices
Smart Irrigation Systems
Sensors
Weather Forecast Servers
Valves
Water Reservoir

## Slide 8: Reasons to Attack Them
They are connected to critical infrastructure (urban/national water service).
To cause financial harm to a party as a result of overconsumption of water (for example, the average combined water tariff in Portland, Oregon is $8.00 .

## Slide 9: Commercial Smart Irrigation Systems Investigated
RainMachine
BlueSpray
GreenIQ (2nd Generation)
Costs $200 on Amazon
6 Zones
Wi-Fi
Costs $249 on Amazon
Touch HD Screen
Up to 16 Zones
Wi-Fi
Costs $205 on Amazon
Up to 16 Zones
Wi-Fi

## Slide 10: Reverse Engineering
Extracting Firmware
  GreenIQ - We downloaded the firmware from its microcontroller’s (Raspberry Pi 2) SD card to our computer using an SD card reader.
  RainMachine - We downloaded the firmware (using UART) to a USB cable.
Analysis - Capturing Network Traffic Using Wireshark
  GreenIQ
  RainMachine
  BlueSpray
(a) RainMachine, (b) GreenIQ, (c) BlueSpray

## Slide 11: Spoofing Attacks
  Spoofing Attack (definition) - a situation in which a person or program successfully masquerades as another by falsifying data, in order to gain illegitimate advantage.
  Purpose
  To change the input of a smart irrigation system in order to water according to the attacker's wishes.
  Execution
  By performing MITM attacks using a bot running on a compromised device that is connected to the same LAN.

## Slide 12: Spoofing Smart Irrigation System Configuration
  A dedicated cloud server is used to provide C&C communication between a device (e.g., smartphone) and GreenIQ.
  A session between GreenIQ and the cloud server is initiated every minute.
HTTP
HTTPS
HTTPS

## Slide 13: Vulnerability Description
  GreenIQ sends an HTTP ping to the cloud server every minute, which is followed by an HTTP response with the timestamp of the last time the user changed the watering plan.
  If the timestamp received doesn't match the one that is stored on GreenIQ (as a result of a user update), GreenIQ sends another HTTP request for the new watering plan, which is followed by an HTTP response sent from the cloud server.

## Slide 14: Vulnerability Description
  Request
  GreenIQ sends a ping every minute with its device ID.
Response
The server sends the timestamp of the last time the watering plan was updated.
GreenIQ
Cloud
Server
3. HTTP Request – Last User Update
Device ID
4. HTTP Response – 1511337789
Timestamp

## Slide 15: Vulnerability Description
Code from GreenIQ’s firmware

## Slide 16: Vulnerability Description
  Request
  GreenIQ requests the new plan and sends its ID.
Device ID
  Response
  The server sends an XML file that contains the user’s information, plans, and configurations.
GreenIQ
Cloud
Server
6. HTTP Response – XML File
5. HTTP Request – (GET) Watering Plan

## Slide 17: Vulnerability Description
MD5
Valid MD5
Plan Changed!
GreenIQ
Cloud
Server
6. HTTP Response – XML File
<?xml version="1.0"?>
<config>
<cmdtime>1526499639</cmdtime>
<master_irrigation>On</master_irrigation>
<data_path>php/users/3720b01effe92174aa55f0cb6fcb82a08cd3ef06d8925e4c458c6839/</data_path>
<weather_dependancy>False</weather_dependancy>
<schedule>
<weekdays>1111111</weekdays> # which days the plan is for
<cycle_period>
<every_x_days>1</every_x_days>
<every_x_hours>2</every_x_hours>
<every_x_minutes>2</every_x_minutes>
</cycle_period>
</schedule>
</config>
<!-- MD5 Signature: 09d13f1c781699fb498c1471f3b8293a -->

## Slide 18: Exploitations and Demo
  Injecting Watering Plans
  Applying an MITM attack to hijack a request that is sent to GreenIQ’s cloud server.
  Sending a newer update time (current time) than the time that is stored on the smart irrigation system.
  Sending a fake XML of a watering plan that consumes water all day long.
1. DNS Request - GreenIQ.net
2. DNS Resolve - GreenIQ.net
4. HTTP Response –
Current Timestamp
3. HTTP Request – Last User Update
6. HTTP Response –
XML File
5. HTTP Request –
(GET) Watering Plan
GreenIQ
Fake
DNS Server
Fake
GreenIQ Cloud Server
DNS Spoofing

## Slide 19: Permanent Denial of Service
1. DNS Request - GreenIQ.net
2. DNS Resolve - GreenIQ.net
4. HTTP Response –
Current Timestamp
3. HTTP Request – Last User Update
6. HTTP Response –
XML File
5. HTTP Request –
(GET) Watering Plan
GreenIQ
Fake
DNS Server
Fake
GreenIQ Cloud Server
DNS Spoofing
Code from GreenIQ’s firmware

## Slide 20: Spoofing Weather Forecast
  A smart irrigation system automatically adapts its watering plan according to the weather forecast obtained from weather forecast services.
  Every 6 hours a weather forecast request is sent to the weather forecast server.
HTTP

## Slide 21: Vulnerability Description
RainMachine automatically adapts its watering plan according to the weather forecast in order to save water.

## Slide 22: Vulnerability Description
  Request
  The client requests a weather forecast from Met.no (weather forecast service) and specifies its GPS coordination.
Response
The server sends an XML file that contains the weather forecast (temperature, humidity, etc.) at hourly resolution.
3. HTTP Request Longitude, Latitude
4. HTTP Response – Weekly Weather Forecast
RainMachine
Weather
Forecast
Server

## Slide 23: Exploitations and Demo
  Request Location Spoofing
  Applying an MITM attack for spoofing the location (so the location appears as if it is the most arid place on Earth).
  Response Spoofing
  Applying an MITM attack for spoofing the forecast weather (so the forecast is incorrect).

## Slide 24: Replay Attacks
  Replay Attack (definition) - a form of network attack in which a valid data transmission is maliciously or fraudulently transmitted.
  Purpose
  To exploit a legitimate HMI interface for C&C as a means of attack in order to water according to the attacker's wishes.
  Execution
  By applying the attack from a bot running on a compromised device that is connected to the same LAN as the smart irrigation system.

## Slide 25: Vulnerability Description
  BlueSpray provides HMI using a dedicated web interface that is based on HTTP protcol to devices that are connected to its LAN.
  It allows the user to schedule watering plans.
  No encryption (HTTP protocol) or authentication is applied.
HTTP
HTTP
LAN (Home Network)

## Slide 26: Format of Schedule Watering Request
  Scheduling watering - JSON format
  {"action":"set",
  "data":[{"enabled":1,"type":2,"program":10,"rpt":[0],"season":0,"cycle":[5,60],"name":"New run","start_date":"2018-06-17","start_time":0,"id":5,"flag":"change"}],
  "msgid":77080}

## Slide 27: Exploitations and Demo
  Generating HTTP request for scheduling watering

## Slide 28: Vulnerability Description
  Opening Valves - The following code was extracted from GreenIQ’s firmware (greeniq_defs.py):
(427) # Testing - Operate Master Valve
(428) set_gpio(MAX_PORTS, gpio_map, '00000010', high_is)
(221) def set_gpio(MAX_PORTS, gpio_map, gpio_command, high_is):
(222) global model_utilities
(223) model_utilities.set_gpio(MAX_PORTS, gpio_map, gpio_command, high_is)

## Slide 29: Exploitations and Demo
  Assuming (1) the SSH password is too weak or has been leaked, or (2) the smart irrigation itself is compromised.
  Opening valves with SSH communication.
SSH
SSH
LAN (Home Network)

## Slide 30: DDoS Attack Against Urban Water Service
Threat Model
C&C model - botnet of smart irrigation systems
Initiating watering from many smart irrigation systems simultaneously

## Slide 31: The Damage
  A typical sprinkler’s water ﬂow is between 0.66 and 4.93 cubic meters per hour (2.795 cubic meters on average)
  What is the damage incurred when the attack is performed using a botnet of smart irrigation system that are triggered to water simultaneously?

## Slide 32: Ethics
  We provided full ethical disclosure of the each of the vulnerabilities that are discussed in this section to GreenIQ, RainMachine, and BlueSpray in June 2018, conveying all of the relevant technical details and some suggestions for addressing the issues raised.
  We received a confirmation of our findings from each of them.
    GreenIQ - GreenIQ thanked us for our findings and decided to apply HTTPS communication between their smart irrigation system and cloud server. In addition, they decided to close the SSH port in their firmware to prevent an attacker from running Python code for watering.
    RainMachine - In June 2018, the Norwegian Meteorological Institute (Met.no) finally upgraded their API to an HTTPS version (replacing the previously used HTTP version). However, other weather forecast services are still HTTP based.
    BlueSpray - BlueSpray responded by asking us to supply details regarding the vulnerability.